## Slide 1
Copyright © 2004 SEDRIS™
Spatial Reference Model (SRM) An Overview http://www.sedris.org/srm.htm
6 January 2004
Lake Buena Vista, Florida
Dr. Ralph M. Toms
SRI International
ISO/IEC 18026 Editor
ralph_toms@sri.com
Dr. Paul Berner
SEDRIS Core Team
ISO/IEC 18026 Editor
Berner@Consultant.com

## Slide 2: SRM tutorial
DESCRIPTION:
The SRM is a unified approach for the representation and use of spatial location information. Designed as a standalone technology, the SRM is a unified approach for the representation and use of spatial location information. Designed as a standalone technology, the SRM provides a complete and concise treatment of the different descriptions of spatial location, and precisely defines the relationship between various spatial reference frames. This tutorial provides a detailed review of the SRM framework and concepts with an emphasis on the modeling implications of different ways of representing spatial location. Challenges and issues in implementing precise and efficient coordinate operations are also discussed.
WHO SHOULD ATTEND:
Those interested in gaining a more complete understanding of the SRM and the theory of accurately representing spatial locations in modeling.
PREREQUISITE:
Prior knowledge of other SEDRIS technologies is not required, however prior attendance at either the "Introduction to SEDRIS for Managers" or "SEDRIS - The Technology Components" tutorial is recommended.
WHAT TO EXPECT:
At completion, the attendee has an appreciation for the complexities involved in accurately representing spatial location. Topics such as object reference models, spatial reference frames, ellipsoids and geoids are covered, among others.

## Slide 3: Prerequisite
To get the most from this tutorial, we assume you know the following, as a prerequisite to this session:
  An understanding of basic mathematical concepts
  An interest in coordinate representation, conversion, and transformation techniques
  Familiarity with the SEDRIS technology components and how they fit together. We assume you have attended:
    “Introduction to SEDRIS for Managers” or
    “SEDRIS - The Technology Components”

## Slide 4: Outline
Introduction
  scope
  goals
SRM Concepts
  key concept preview
  object-space and position-space
  reference datums and object reference models
  coordinate systems
  spatial reference frames
  vertical offset surfaces
  spatial operations and the API
Computational considerations
Spatial operation validity, conformance, accuracy
Structure of the SRM ISO standard

## Slide 5
The Spatial Reference Model (SRM) is a general concept
There are two aspects of the SRM discussed in this tutorial
• One aspect is the SRM as an International Standard.
- ISO/IEC 18026 Spatial Reference Model.
- Under development, the final committee draft is to be released summer ‘04.
- This tutorial uses the nomenclature, definitions and
concepts of ISO/IEC 18026.
- Consistency with other International Standards is promoted.
- Efficiency of algorithms or their implementation is not part of the
ISO/IEC 18026 specification.
• Another aspect is the implementation of the SRM in SEDRIS
- The SEDRIS implementation is designed to be compliant with the
emerging 18026 International Standard.
- The SEDRIS implementation is an application driven development.
- A software architecture and spatial operations API is required.
- Algorithms for spatial operations in spatial frames are designed to be accurate robust and efficient.
- The SEDRIS software has been subject to extensive testing.

## Slide 6: In the beginning ...
Defining and using a consistent spatial reference framework is critical for simulation interoperability
  System models (men, equipment, material, …)
  Environmental: data, models, phenomena
At all levels of simulation detail/resolution
  Aggregated / Entity; Constructive / Virtual / Live
Systems
Systems, where?
Systems, and what else?
The environment starts with locating your systems; sometimes that’s about all you could afford in legacy simulations.
The environment continues with defining the context within which systems interact; and that context
can advantage, or disadvantage,
them ...
The void ...
Notes: 2
8

## Slide 7
Why is a Spatial Reference Model (SRM) needed?
The Modeling & Simulation (M&S) community has not been consistent in the treatment of models of the Earth and related coordinate systems.
Consistency is required for joint distributed simulation in order to:
  Achieve a reasonably level playing field,
  To support meaningful VV&A.
A number of different Earth reference models (ERMs) are currently employed and this affects:
  Representation of the environment in M&S and authoritative data bases.
  Dynamics formulations, both kinematics and kinetics (movement).
  Acquisition modeling and processing (inter-visibility).
Loss-less and accurate spatial operations are critical to representation and interchange of location data.
A nomenclature inconsistency exists.
  For example, how do these variables relate? Altitude, elevation, height, geodetic height, ellipsoidal height, orthometric height, height above sea level, height above mean sea level, terrain height, pressure altitude, temperature altitude, nap of the Earth, ...

## Slide 8: Other interoperability examples
It isn’t just simulations that have potential interface problems due to spatial referencing.
Real (embedded) systems also need to communicate spatially referenced data.
Test range operation is another application domain where consistent spatial referencing is important, particularly if multiple ranges share real-time information.
The federation of live, virtual and constructive
systems requires a standardized SRM.

## Slide 9: Why is accuracy needed for coordinate transformations?
* Lucha, G. V., On the Consequences of Neglecting Measurement
Accuracy Issues in Live and Virtual interactions”, SIW Spring 1997
In the past, it has been difficult to measure positions on the surface of the Earth to better than 1 metre.
  This situation is changing due to new technology developments.
  GPS now can achieve absolute accuracy of about 21 cm (SEP 90%) over large regions.
Real-world applications mostly use relative coordinate systems
  Dynamically correct location errors by using on-board sensors.
In the simulation environment, both absolute and relative spatial referencing must be accurately portrayed.
Mixing of live & synthetic environments has special accuracy requirements*.
Mission planning, rehearsal, & conduct of real operations have situation-dependent accuracy requirements.

## Slide 10: Target shooting at a visible target in the real world
Never used any precise location or environmental data.
Set up paper target with aim-point approximately 1000 metres away.
Shoot N rounds.
Measure miss distances using bullet holes on paper target, and compute CEP or some other measure of accuracy.
(Relative coordinate system)

## Slide 11: Simulation of target shooting at a visible target
Any errors made in any of the position-location computations,
including those needed to compute the correct environmental
parameters, can and will dilute the accuracy of the result.
Select lococentric Euclidean 3D CS, origin at the shooter.
Define coordinates of the target & shooter.
  Both with target plane oriented perpendicular to line of sight.
Develop an aiming model with random inputs.
Define shoot time, T.
Integrate bullet trajectory in time, from T until it pierces the plane of the target (need air temperature, density, speed of sound, wind, etc.)
  May have to access geodetic system for each of the environmental parameters.
  Will need an iterative scheme to get the impact point.
Compute radial miss at target plane impact.
(Simulation of a relative coordinate system)

## Slide 12: Servicing a non-visible target in the real world
Use location data but no precisely measured environmental data.
Simulation of this scenario requires detailed dynamics
and environmental models
The problem: An artillery piece shoots at a target coordinates provided from an external source.
The shooter has its location in some coordinate system, e. g. Augmented TM.
The target coordinates may be known to some accuracy in geodetic latitude, longitude & geodetic height.
The fire control system may or may not require conversions to another coordinate system, for example a lococentric Euclidean 3D coordinate system.
The fire control system computes firing angles based on its internal mechanization and may model wind, air density and other environmental parameters.
The round impact and miss distances are observed by a forward observer who feeds information back to the firing site.
The process is completed when the impact error is small enough.

## Slide 13: Augmented Transverse Mercator(ATM) example
The results of such elevation angle and range distortions may not be so apparent when all simulations involved use ATM. However, in a federation involving real world coordinate systems the distortions may become evident. Use of ATM increases visibility, causes interactions to prosecute too fast, leads to an uneven playing field and is not recommended for use in joint simulations.
90o East
•
•
•
•
plane of the projection
Central Meridian
TM plane inset to
reduce average distortion
(scale factor 0,9996 at the
central meridian)
Several distortions are introduced, especially at the higher latitudes.

## Slide 14: SRM requirements
Completeness, must:
  include coordinate systems in wide usage.
  tie those systems together into a commonly used framework.
  educate the system developer.
    E.g., What’s a horizontal datum, a vertical datum, a geoid?
Accuracy
  Generally higher than required for C4ISR systems.
  E.g., Typically better than 1 cm. up past geosynchronous orbit (nominally 1 mm near the ERM surface).
  Computation of operations in spatial frames must not impact
  application validity.
Performance
  Never fast enough!
  Many environmental data sets dominated by location data.
    Therefore efficient inter-conversion is key to meeting 72 hour “ready-to-run” mandate.
  Federate costs for distributed simulation using heterogeneous coordinate systems can be substantial (e.g., 20% or more).
SEDRIS algorithms and implementations are very accurate and 2-5x faster than algorithms/implementations reported in the literature.
Notes: 3
9

## Slide 15: Location is not enough
The key in Modeling and Simulation is not so much where things are, but what they can interact with …
  Remembering that “what” includes both systems and components of the environment itself
A complete SRM must address:
  Location
  Distance (range, line of sight, geodesics…)
  Vector quantities, such as direction
  (azimuth and elevation angle)
Location interconversions between common spatial reference frames do not necessarily preserve these.
Systems, and what else?
The environment continues with defining the context within which systems interact; and that context can advantage, or disadvantage, them ...

## Slide 16: The scope of the SRM
The SRM is developed to include spatial referencing for any real or conceptual object in the solar system, or any abstract or virtual universe.

## Slide 17: It’s a Loooong way up
MESOSPHERE
STRATOSPHERE
U-2
TROPOSPHERE
RADIATION BELTS
25+ Satellites
GPS
IONOSPHERE
25+ Satellites
DMSP
SHUTTLE
MAGNETOSPHERE
30+ Satellites
DSP
MILSTAR
DSCS
Terrestrial Weather
Space Weather
S
E
A
M
L
E
S
S
E
N
V
I
R
O
N
M
E
N
T

## Slide 18: The SRM encompasses more than the Earth

## Slide 19: The SRM requires a shared solution
This situation/problem is not unique to M&S.
  E.g., precise positioning for navigation, range tracking,…
A “worldwide problem”
  Being tackled by ISO/IEC JTC 1/SC 24/WG 8.
  ISO/IEC 18026: Spatial Reference Model (SRM)
  See the following URLs for more information:
  http://www.iso.ch
  http://www.jtc1.org
  http://isotc.iso.ch/livelink/livelink.exe?func=ll&objId=327973& objAction=browse&sort=name
  http://www.sedris.org/wg8home
If you have spatially located data,
  Who doesn’t?
Then you need to understand spatial referencing,
  A very complex topic (as we’ll demonstrate)
Especially if you intend to interchange data.

## Slide 20: SRM goals
Unambiguous Spatial Referencing
  locations and directions
  well defined terminology
A single framework for diverse communities of users
  CAD/CAM
  modeling and simulation
  geodesy
  space science
Extensibility
  including an extensible API
  a standardized registration process

## Slide 21: SRM concepts

## Slide 22: Key concepts (Preview)
Spatial
Coordinate
System
Abstract
Coordinate
System
object-space
spatial
object
position-space
Embedding

## Slide 23: Key concepts (Preview)
Embedding
object-space
spatial
object
position-space
object reference model
reference datum
reference datum
reference datum

## Slide 24: Key concepts (Preview)
Spatial Reference Frame
object-space
spatial
object
object reference model
reference datum
reference datum
reference datum
Coordinate
System

## Slide 25: SRM concepts
Spatial objects and object-space
Position-space and normal embeddings
Reference datums
Object reference models
Coordinate systems
  Abstract coordinate systems
    localization
    Induced surface coordinate systems
    map projections
  Temporal coordinate systems
  Spatial coordinate systems
Spatial reference frames
Vertical offset surfaces
Spatial operations
Spatial objects and object-space

## Slide 26: Spatial objects and object-space
Object-space:
The real or abstract universe that contains a spatial object.
spatial object
(A spatial object is assumed to be fixed in its object-space.)

## Slide 27: Spatial objects and object-space
spatial object
physical object
abstract object
The length of a metre has
intrinsic meaning.
The length of a metre length
does not have intrinsic meaning.
“real world”
engineering models,
virtual world,
CAD,...
Length scale shall
be defined.

## Slide 28: SRM concepts
Spatial objects and object-space
Position-space and normal embeddings
Reference datums
Object reference models
Coordinate systems
  Abstract coordinate systems
    localization
    Induced surface coordinate systems
    map projections
  Temporal coordinate systems
  Spatial coordinate systems
Spatial reference frames
Vertical offset surfaces
Spatial operations

## Slide 29: Position-space and embeddings
Position-space:
An n-dimensional Euclidean space abstraction of object-space.
object-space
p
x-axis
z-axis
y-axis
position-space
embedding:
A particular position-space model of object space.
x-axis
z-axis
y-axis
p
embedding

## Slide 30: Position-space and embeddings
x-axis
z-axis
y-axis
position-space
(x, y, z)
An embedding allows position-space operations and methods of
algebraic geometry to be applied to object-space.
An embedding is a function from position-space to object-space.
object-space
p
An embedding is normal if distance is preserved assuming 1 Euclidean unit = 1 metre in object-space.
In the 3D case, an embedding is either right-handed or left-handed.

## Slide 31: Position-space and embeddings
object-space
p
There are infinitely many normal embeddings of a given object-space.
In general, no one normal embedding is intrinsic or canonical.
x-axis
z-axis
y-axis
p
normal embedding 1
p
normal embedding 2
x-axis
z-axis
y-axis

## Slide 32: Position-space and embeddings
Given two normal embeddings, E1 and E2
how are are they related to each other?
Each Tk is a rotation matrix ...
7-parameter transformation:

## Slide 33: 7 parameter transformation
Relates embedding E2
to embedding E1

## Slide 34: SRM concepts
Spatial objects and object-space
Position-space and normal embeddings
Reference datums
Object reference models
Coordinate systems
  Abstract coordinate systems
    localization
    Induced surface coordinate systems
    map projections
  Temporal coordinate systems
  Spatial coordinate systems
Spatial reference frames
Vertical offset surfaces
Spatial operations

## Slide 35: How are embeddings specified?
The specification pieces
  Reference Datum (RD)
  Spatial binding
RD and normal embedding compatibility
“Assembly instructions”:
  Object Reference Model Template (ORMT)
Object Reference Model (ORM)
  ORMT Realization
  Embedding specification

## Slide 36: Reference datums
Reference datum (RD):
A geometric construct in position-space
that is used to specify an aspect of an embedding
of position-space into object-space.

## Slide 37: Reference datum (RD)
Concept
  A construct with position-space analytic representation and object-space geometric representation
  Category:
    Point
    Directed curve
    Oriented surface
  Expressed as implicit or explicit function of position-space
  Method of orientation (except point)
  Method of binding to object is application domain specific and is outside of SRM scope
Standardized set
  Label, code, definition
  set of Ellipsoid RD associated to celestial objects

## Slide 38: Reference datum (RD)

## Slide 39: 3D point RDs

## Slide 40: 3D directed curve RDs

## Slide 41: Oriented surface RD (planes)

## Slide 42: Oriented surface RD (ellipsoids)
Oblate: a > b
Sphere: a = b
Prolate: a < b
Example:
RD_AIRY Airy 1830
a = 6 377 563,396 flattening = 1/299,324 964 6
flattening = (a-b)/a
b = a·(1-flattening)

## Slide 43: Standard reference datums
RD
Point
Reference Datum:
a simple geometric construct in position-space that can be bound to
object-space.
XZ-plane
Directed Line
Plane
Ellipsoid RD
Origin
Y-axis
(0, 0, 0)
X-axis
F(t)=(0, t, 0)
F(t)=(t, 0, 0)
Z-axis
F(t)=(0, 0, t)
OBE
Etc.
Sphere
PRS
Oblate
Ellipsoid type:
semi-major axis,
flattening, date
Sphere
type:
radius,
date
Prolate
Ellipsoid
type
Airy 1830
Clark 1880
North American 1983
WGS84 Ellipsoid
International 1924
Etc.
NOGAPS
MM5
MODTRAN Mid Latitude
Reference Spheres
and Ellipsoids
Etc.
Oriented surface

## Slide 44: RD bindings
An RD is bound when the RD is identified with a
corresponding constructed entity in object-space.
Points are bound to identified points, directed curves to constructed curves, and oriented surfaces to constructed surfaces.

## Slide 45: RD bindings and embedding compatibility
x-axis
z-axis
y-axis
p
embedding is not compatible
An RD is compatible with a normal embedding if
the locus of the RD in position-space is coincident with
the points (and direction or orientation, as applicable)
of the geometric construction of the binding.
x-axis
z-axis
y-axis
binding
RD_3D_XY_PLANE

## Slide 46: RD bindings and embedding compatibility
p
embedding is compatible
x-axis
z-axis
y-axis
binding
RD_3D_XY_PLANE
x-axis
z-axis
y-axis
An RD is compatible with a normal embedding if
the locus of the RD in position-space is coincident with
the points (and direction or orientation, as applicable)
of the geometric construction of the binding.

## Slide 47: Object reference models
The set of normal embeddings compatible with a single RD binding has many members.
The set of normal embeddings compatible with a set of 2 or more RD bindings may be empty.
A careful selection of RDs and bindings may result in a compatible set of normal embeddings consisting of a single member. I.e.: There is a unique compatible embedding for the bound RD set.
This is the concept for an object reference model.

## Slide 48: Object reference models
Object reference model (ORM) for a spatial object:
A set of RDs bound by identification with geometric constructions in object-space for which there exists exactly one normal embedding of position-space into object-space which is compatible with each RD
binding in the set.
In the 3D case, this unique embedding shall also be right-handed.

## Slide 49: Object reference model template
An object reference model template (ORMT), is a set of RD components, together with binding constraints which will determine a unique normal embedding of position-space into object-space when an instance of each the RD components is bound to corresponding geometric constructs in object-space that conform to the binding constraints.
  If the position-space is 3D, the unique normal embedding shall be right-handed.
A binding constraint is a specification of relationships in object-space between geometric constructs corresponding to RD instances.
  The binding constraint specification may include containment of a point in a curve, or a surface, or a curve in a surface, coincidence of a line with the axis of symmetry of a surface, the right-handedness of sets of directed lines or oriented planes, or the distance in object-space between points.

## Slide 50: ORMT example

## Slide 51: Realization of an ORMT
RDS
  RDS
    Oblate ellipsoid instance
    XZ-plane
  Binding Rule
    the ellipsoid minor axis must be contained in the plane.
Binding
  There is only one place in Earth’s space for the RDS with:
    ellipsoid minor axis points parallel to Earth’s rotational axis
    The point is on the ellipsoid surface with given long/lat
    The surface normal at the point points in the given direction.
The binding creates an
indirect normal embedding
of 3D position-space
The actual binding
methodology
is not part of the SRM

## Slide 52: 3D ORMTs
ORMT_3D_SPHERE
  3D sphere with designated directional axis and xz-plane
ORMT_3D_OBLATE_ELLIPSOID
  3D oblate ellipsoid with designated minor axis direction and xz-plane
ORMT_3D_PROLATE_ELLIPSOID
  3D prolate ellipsoid with designated major axis direction and xz-plane
ORMT_3D_BI_AXIS_ORIGIN
  x- and y-axes determined by directed perpendicular lines passing through the origin
ORMT_3D_TRI_PLANE
  Origin determined by the intersection of three planes

## Slide 53: standard ORMs
Each standardized ORM is a realization of a standard ORMT
Concept
  ORMT realization bound to a specific object at a specific time
    Intrinsically determines a unique (right-handed) normal embedding
  Name of object, definition, RD components
  Object binding
Standard/registered ORMs
    Label, code, definition, region, epoch, etc.
    Standard ellipsoid RD (if so based)
    Reference transformation(s) specified with respect to the object reference ORM by 7 parameter values:
        origin offset (x, y, z)
        axis rotations (1,  2,  3)
        scale adjustment s
Every spatial object has one reference ORM
    The WGS 84 ORM is the Earth reference ORM

## Slide 54: ORMT realization example
North American 1927 (NAD 27)
  ORMT_3D_OBLATE_ELLIPSOID
    Oblate ellipsoid RD instance: Clark 1866 ellipsoid
      semi-major axis 6378206.4 m
      inverse flattening 294.9786982
  Binding (not part of the SRM specification)
    Meades Ranch, Kansas on the oblate ellipsoid surface with long=98°32’30.506” W, lat=39°13’26.686” N and surface normal = -1.32 =1.93.
  ORM reference transformation:
    specification of the binding by 7 parameters w.r.t WGS 84 ORM
      origin offset: x = -8, y = 160, z = 176
      axis rotations 1= 0,  2 = 0,  3 = 0
      scale adjustment s = 0

## Slide 55: Binding categories
A binding restriction for an ORMT is an object specific restriction for the binding of a single RD in the RD set of the ORMT.
A binding category is an ORMT with:
- a binding category name,
- a set of binding restrictions for the ORMT, and
- object restrictions which delineate the objects for which the binding restrictions apply.
Example: The equatorial inertial dynamic binding category

## Slide 56: ORMs vs. object models
Reference Surface: An ORM is often selected to contain one or more RDs of category oriented surface to correspond to (physical or conceptual) surface(s) which is significant to the modelled spatial object.
Example: an oblate ellipsoid as a model of the shape of the Earth.
An RD is chosen and its position with respect to the object is bound so that the RD instance is a “best fit” to the object in some application-specific sense.
In particular, if the RD surface is “fitted” to a specific part of the object surface, the ORM is a local model.
If the RD is selected to best fit the entire surface, the ORM is a global model.
Other Surface models:
  geoid: gravity equipotential surface that approximates the mean sea level of the Earth.
  pressure equipotential surface: equipotential surface of a pressure field.
  topographic surface: interface between the solid and liquid/gas portions of a celestial object.
Some of these surfaces are treated in the SRM as vertical offset surfaces (a later topic), while others are outside of the scope of the SRM.

## Slide 57: SRM concepts
Spatial objects and object-space
Position-space and normal embeddings
Reference datums
Object reference models
Coordinate systems
  Abstract coordinate systems
    localization
    Induced surface coordinate systems
    map projections
  Temporal coordinate systems
  Spatial coordinate systems
Spatial reference frames
Vertical offset surfaces
Spatial operations

## Slide 58: Coordinate Systems (CS)
An abstract CS is a means of identifying a set positions in m-dimensional position-space (1  m  3) that is comprised of:
  a. a CS domain,
  b. a generating function, and
  c. a CS range,
where:
  d. the CS domain is a connected domain in the Euclidean space of n-tuples (1  n  m), called the coordinate-space,
  e. the generating function shall be a one-to-one, smooth, orientation preserving function from the CS domain onto the CS range, and
  f. the CS range is a sub-set of position-space.

## Slide 59: Coordinates for position-space
r

r sin 
r cos 
X
Y
Geometric/Trigonometric
derivation
Generating function
realization
Not all CSs have Geometric/Trigonometric derivations

## Slide 60: Coordinate system type

## Slide 61: Coordinate system characteristics
A CS is linear if it has an affine generating function
(a function is affine if it is a translation operator plus a linear operator)
A non-linear CS is curvilinear.
A linear CS is orthonormal if
3D CS case: the coordinates (1,0,0), (0,1,0),
and (0,0,1) are length one and mutually
perpendicular in position-space.
Surface and 2D CS case: the coordinates (1,0),and (0,0,1)
are length one and mutually perpendicular
in position-space.

## Slide 62: Spherical CS specification Part 1

## Slide 63: Spherical CS specification Part 2

## Slide 64: Lococentric spherical CS
Spherical CS
Lococentric Spherical CS
Position-space
origin
Lococentric
origin
Fs(, , )
FLS(, , )=L3D(Fs(, , ))
Localization operator:

## Slide 65: Coordinate surfaces and curves
Curve: GC1(u) = G(u, v0, w0).
Curve: GC2(v) = G(u0, v, w0).
Curve: GC3(w) = G(u0, v0, w).
3D CS generating function: G(u, v, w).
Surface 1: GS1(u, v) = G(u, v, w0).
Surface 2: GS2(u, v) = G(u, v0, w).
Surface 3: GS3(u, v) = G(u0, v, w).
Each GSk is the generating function for a surface CS.
Each GCk is the generating function for a curve CS.
A CS is orthogonal if its coordinate curves intersect at right angles.

## Slide 66: Coordinate surfaces and curves
Example: Geodetic G(, , h)
Ellipsoid: GS(, ) = G(, , 0).
parallel: GC1() = G(, 0, 0).
meridian: GC2() = G(0, , 0).
3D geodetic
(induced)
Surface geodetic

## Slide 67: Map projections
Map projections are 2D models of a 3D curved surface.

## Slide 68: Map projections
A map projection (MP) is comprised of
    a. a connected region of the surface of an oblate ellipsoid, b. a generating projection, and c. an MP range in 2D coordinate-space,
where:
    d. the MP range is connected, and e. the generating projection is one-to-one from the region of the oblate ellipsoid onto its MP range and its inverse function is smooth and orientation preserving.
Map projections are 2D models of a 3D curved surface.
The generating projection is formulated in terms of surface geodetic coordinates called mapping equations.

## Slide 69: Map projections
Map projection coordinate-space geometry
models/approximates oblate ellipsoid
surface geometry.
But the model geometry is distorted.
Map projections are 2D models of a 3D curved surface.

## Slide 70: Map projection distortion
Length distortion
  The ratio of map distance to geodesic distance is not constant.
  “Equidistant” map projections have a constant distance ratio in one direction (E.g.: North/South distances)
Angular distortion
  A map projection may or may not preserve angles.
  A map projection is conformal if it preserves angles.
Area distortion
  The ratio of map area to ellipsoid area may not be constant.
  “Equi-area” map projections have a constant area ratio.

## Slide 71: Map projections
Quantifying distortion:
Map distance vs geodesic distance
  point scale
    ratio at a point for “infinitesimal” distances
    varies at different points
    varies by direction in non-conformal map projections
  map scale
    Nominal ratio for the map area
map azimuth vs. geodetic azimuth
Convergence of the Meridian (COM)

## Slide 72: Azimuth
map azimuth b geodetic azimuth a
Mercator Map Projection
a
b

## Slide 73: Convergence of the Meridian
The convergence of the meridian  is the angle between MP “North” and true North on the ellipsoid (positive clockwise)
u
v


## Slide 74: Map projection as a surface CS
generating function
GMP = GGD Q
geodetic generating function

## Slide 75: Augmented map projections
Simulations usually require three dimensions.
Some coordinate systems three dimensional by definition.
Map projections (two surface dimensions) are commonly augmented with a vertical axis to create a three dimensional system.
Various vertical measures are used for these augmentations, such as:
  Mean sea level height, orthometric height, geodetic height, pressure altitude, and others.
These augmentations may be in different units than the other two axes so that the resulting CS may be vertically distorted.
This practice adds additional geometric distortions (now in the third dimension).
Augmented map projection coordinate-space has a (linear) vector space structure, but the CS is a curvilinear CS.

## Slide 76: Augmented map projections
Augmenting map coordinates
with ellipsoidal height produces a 3D CS.
MP coordinate (u, v)
(, ) surface geodetic coordinate
Augmented
MP coordinate (u, v, h)
(, , h) 3D geodetic coordinate
Caution!
Augmented map geometry
in coordinate-space must not be confused with position-space geometry

## Slide 77: Augmented map projections
(
u
1
,
v
1
,
w
)
(
u
1
,
v
1
, 0)
(
u
2
,
v
2
,
w
)
(
u
2
,
v
2
,
0)
coordinate -space
position-space
p
p’
q’
q
Line of sight visibility in
augmented map projection coordinate space...
… can be an illusion.

## Slide 78: Geometry: coordinate-space vs. position-space
A cube in an augmented
map projection coordinate-space ...
… is not a cube position-space.
Only points in the red region are transformed by the map projection.
Every point on the base (red) is on the ellipsoid.
If the projection is conformal interior angles of the base are 90°.
All other angles are generally not 90°.
In general none of the sides are equal.
The vertical lines are not parallel and are not even coplanar.
The 3D volume is no longer convex.
Every point on the base (red) is on the plane.
Interior angles of the base are 90°.
All other interior angles are 90°.
All sides are of the same length.
The vertical sides are parallel planes.
The cube is a convex hull.

## Slide 79: Standard coordinate systems
3D CS
Euclidean 3D
Lococentric Euclidean 3D
Spherical
Lococentric spherical
Azimuthal spherical
Lococentric azimuthal spherical
Geodetic 3D
Cylindrical
Lococentric cylindrical
Surface CS
Surface geodetic
Lococentric surface Euclidean
Lococentric surface azimuthal
Lococentric surface polar
Euclidean 2D
Lococentric Euclidean 2D
Azimuthal
Lococentric azimuthal
Polar
Lococentric polar
Euclidean 1D
Euclidean 1D
Mercator
Oblique Mercator
Transverse Mercator
Lambert conformal conic
Polar stereographic
Equidistant cylindrical
Map projection CS
2D CS
1D CS:
Plus those that will be registered
with the ISO standard.

## Slide 80: Surface CS induced on a coordinate surface
Geodetic 3D
  Surface geodetic induced on h = 0 surface.
Augmented Map projection
  Map projection induced on h = 0 surface.
Cylindrical
  Surface Polar induced on z = 0 surface.

## Slide 81: Temporal CS
An integrated temporal coordinate system
is a Euclidean 1D CS based on a unit of duration
that is derived from a physical phenomenon.
Fixing an origin (called the epoch) and then continuously
accumulating units of the duration specifies an
integrated temporal coordinate system.
The time continuum
epoch
0

## Slide 82: Spatial coordinate systems
Abstract CS + position-space normal embedding
= Spatial CS

## Slide 83: Spatial coordinate systems
p
3D case

## Slide 84: Spatial coordinate systems
3D case

## Slide 85: Spatial coordinate systems
3D case

## Slide 86: SRM concepts
Spatial objects and object-space
Position-space and normal embeddings
Reference datums
Object reference models
Coordinate systems
  Abstract coordinate systems
    localization
    Induced surface coordinate systems
    map projections
  Temporal coordinate systems
  Spatial coordinate systems
Spatial reference frames
Vertical offset surfaces
Spatial operations

## Slide 87: Spatial reference frame (SRF)
When a CS is bound to the embedding specified by an ORM, the result is called a
Spatial Reference Frame.
Concept

## Slide 88: Spatial reference frame
Specification
  An ORM with a compatible CS binding
    Example: Ellipsoid based CS is compatible with Ellipsoidal ORM only.
    CS binding: ORM determines (some) CS parameters.
    Example: geodetic parameters a, b are set to oblate ellipsoid major and minor semi-axis values
  Adds additional domain CS restrictions
    Example: Restrict to a specific region
      Optionally specify a coordinate valid region
      Optionally specify a coordinate extended valid region
  Values for remaining CS parameters
    If any CS parameters are not bound by the ORM

## Slide 89: Celestiodetic SRF
geodetic 3D CS
+
Parameter binding to the ellipsoid of a ellipsoidal ORM

celestiodetic SRF
Example:

## Slide 90: Celestiodetic SRF
Geodetic CS
parameters:
a, b
Bound to
ORM
oblate ellipsoid RD
parameters:
a, b

## Slide 91: Local tangent space Euclidean SRF
Lococentric Euclidean 3D CS
+
Parameter binding to the ellipsoid of a ellipsoidal ORM

Local tangent space Euclidean SRF
Example:

## Slide 92: Local tangent space Euclidean SRF
x-axis
z-axis
y-axis
position-space (x, y, z)
t
q
r
s
Lococentric Euclidean 3D CS
parameters:
vectors q, r, s
(t = r x s)
u-axis
v-axis
w-axis
Lococentric Euclidean 3D CS
coordinate: (u, v, w)

## Slide 93: Local tangent space Euclidean SRF
(, )
SRF
parameters: , 
ellipsoid ORM
Use ORM to bind
CS parameters:
vectors q, r, s
vectors s and t, lie in
the tangent plane
r is normal to the surface
t
q
r
s

## Slide 94: Local tangent space Euclidean SRF
u-axis
v-axis
w-axis
(, )
The resulting SRF

## Slide 95: Local tangent space Euclidean SRF
w-axis
(, )
Additional SRF
parameters:
u-axis
v-axis


: azimuth

## Slide 96: Local tangent space Euclidean SRF
w-axis
(, )
Additional SRF
parameters:
u-axis
v-axis


: azimuth
h0: offset height
h
h
h
w-axis
u-axis
v-axis

## Slide 97: Local tangent space Euclidean SRF
w-axis
(, )
Additional SRF
parameters:
u-axis
v-axis


: azimuth
h0: offset height
h
h
h
w-axis
u-axis
v-axis
uF: false easting
vF: false
northing
u-axis
v-axis
w-axis
uF
vF
w-axis
u-axis
v-axis

## Slide 98: Local tangent space Euclidean SRF
Algebraic specification of the parameter binding

## Slide 99: Canonical Local tangent space Euclidean SRF
Given any SRF based on an oblate ellipsoid ORM (or sphere ORM),
and a point (o, o) on the ellipsoid, the Canonical Local tangent space Euclidean (CLTSE) SRF at ( o,  o) is the
Local tangent space Euclidean SRF with parameters:
 = o
 = o
 = 0
h0 = 0
uF = vF = 0
CLTSE SRFs are useful for defining a vector direction in
an SRF with a curvilinear CS.
CLTSE SRFs also useful in instancing an abstract model at a point in an SRF. (E.g.: SEDRIS DRM Geometry/Feature Model Instance.)

## Slide 100: SRF templates
SRF Template (SRFT)
  ORM constraints and CS parameters binding.
    Unbound CS parameters (if any) become SRFT parameters.
SRF instance of a template
  ORM specified, and
  SRFT parameters are specified.
  All standardized SRF in the SRM are SRFT instances.
SRF sets
  A fixed (standard/registered) indexed set of SRFT instances for a given ORM.
  Examples : UTM - zone code and hemisphere GCS - index code PS - polar aspect code

## Slide 101: SRFTs for 3D object-space
Celestiocentric
Local space rectangular 3D
Celestiodetic
Local tangent space Euclidean
Local tangent space azimuthal spherical
Local tangent space cylindrical
Celestiomagnetic
Equatorial inertial
Solar ecliptic
Solar equatorial
Solar magnetospheric
Solar magnetic
Heliospheric Aries ecliptic
Heliospheric Earth ecliptic
Heliospheric Earth equatorial
(augmented) Map projections
Mercator
Oblique Mercator
Transverse Mercator
Lambert conformal conic
Polar stereographic
Equidistant cylindrical
Plus those that will be registered
with the ISO standard.

## Slide 102: SRFTs for 3D object-space
3D CS SRF
Celestiodetic
Local tangent space Euclidean
Local tangent space azimuthal spherical
Local tangent space cylindrical
(augmented) Map projection SRF
Mercator
Oblique Mercator
Transverse Mercator
Lambert conformal conic
Polar stereographic
Equidistant cylindrical
(induced) surface CS SRF
surface Celestiodetic
Local tangent plane Euclidean
Local tangent plane azimuthal
Local tangent plane polar
(surface) Map projection SRF
Mercator
Oblique Mercator
Transverse Mercator
Lambert conformal conic
Polar stereographic
Equidistant cylindrical
Surface CS SRFs induced by 3D CS SRFs
Compare with ISO 19111 concept of a compound CRS

## Slide 103: SRF example
ORM
  North American 1927 (NAD 27)
    includes: NAD 27 ellipsoid RD (Clark 1866 ellipsoid)
CS
  Lambert conformal conic map projection
SRF parameters (unbound CS parameters)
    longitude of origin 97º West
    latitude of origin 38º North
    central scale 1
    false easting 0
    false northing 0
Additional CS domain/range constraints:
  Restricted to CONUS (expressed as min/max values for map coordinates u and v)
Using Lambert conformal conic SRFT

## Slide 104: SRFTs for 2D object-space
Local space rectangular 2D
Local space azimuthal
Local space polar

## Slide 105: Reference vectors
Represent a direction in object space
Must have reference position
Defined in SRFs with a linear CS:
  Celestiocentric, Local Tangent Space Euclidean (LTSE), Local Space Rectangular
In other cases, defined in Canonical LTSE SRF at the reference location
The “direction” (0,0,1)
depends the
reference location
(p or q)

## Slide 106: Reference vectors
Reference vectors are used to specify spatial directions.
In the SEDRIS DRM, reference vectors are restricted to unit vectors associated with a reference position (point).
Reference vectors are specified in the 3D Orthonormal CS of the CLTSE determined by the reference position.
Reference vectors and directions in general must be transformed when changing SRFs.

## Slide 107: SRM concepts
Spatial objects and object-space
Position-space and normal embeddings
Reference datums
Object reference models
Coordinate systems
  Abstract coordinate systems
    localization
    Induced surface coordinate systems
    map projections
  Temporal coordinate systems
  Spatial coordinate systems
Spatial reference frames
Vertical offset surfaces
Spatial operations

## Slide 108: Earth surfaces
Topographic Surface is the interface between the solid and liquid/gas portions of the Earth. It corresponds to the surface of the land and the floor of the ocean.
In the SRM, there is no Earth; there are only models of the Earth.
Geoid Surface excludes the topographic surface, and therefore generally corresponds with mean sea level.
Ellipsoid RD
Normal
(to the
Ellipsoid)

## Slide 109: Vertical offset model (VOM)
A VOM is a smooth surface defined by a function the embedded position-space of an ORM
A VOM models a reference surface
  I.e. Mean sea level, gravity equi-potential surface, etc.
Example:
  The geiod for WGS 84 ORM

## Slide 110: Vertical offset model (VOM)
Can be used to modify height for a composite SRF:
h
he
(,)
v(,)
p
Ellipsoidal height coordinate curve
Geiod (vertical offset surface)
Ellipsoid RD of the ORM
ellipsoidal height h  elevation he = (h- v(, ) ) where v(, ) is the geiodal separation value

## Slide 111: SRM concepts
Spatial objects and object-space
Position space and normal embeddings
Reference datums
Object reference models
Coordinate systems
  Abstract coordinate systems
    localization
    Induced surface coordinate systems
    map projections
  Temporal coordinate systems
  Spatial coordinate systems
Spatial reference frames
Vertical offset surfaces
Spatial operations

## Slide 112: Spatial operations
Change SRF
  Coordinate representation
    includes as special cases: coordinate transformation coordinate conversion
    coordinate validity
  Direction representation
  Change position-space embedding
Map projection based SRFs
  map and geodetic azimuth
  point scale
  Convergence of the Meridian
Euclidean and geodesic distance

## Slide 113: Change of embeddings
ORM1 Embedding position
Object reference ORM Embedding position
Reference 7 parameter transformation
ORM2 Embedding position
Inverse reference 7 parameter transformation
H
H is a vector addition
and a matrix multiply
(Reference ORM for Earth is WGS 84 ORM)
Case: object-fixed ORMs for same object

## Slide 114: Change of embeddings
ORM1 Embedding position
ORM2 Embedding position
H
H is a vector addition
and a matrix multiply
Case: dynamic ORMs or two different objects
Assuming a fixed time coordinate t = to in the dynamic case:
H=H(to)

## Slide 115: Coordinate transformation
(
f
,
l
,
h
) or
(
f
’
,
l
,
h’
)
b
meridian of (
l
)
f
l
a
a
h
•
b'
f
’
•
h’
b’
<
b
f
<
f
’
h
<
h’
•
Different ORMs (same celestial object)
Same CS

## Slide 116: Change SRF operations
Source coordinate
in CS1
CS1 Generating function
ORM1 Embedding position
Target coordinate
in CS2
CS2 Inverse Generating function
ORM2 Embedding position
SRF1 = ORM1 + CS1
SRF2 = ORM2 + CS2
H
Coordinates

## Slide 117: Coordinate conversion
(
f
,
l
,
h
)
or
(
x
,
y
,
z
)
z-axis
b
f
l
a
h
•
x
y
z
•
Same ORM
Different CS
x-axis
y-axis

## Slide 118: Change SRF operations
Source coordinate
in CS1
CS1 Generating function
Target coordinate
in CS2
CS2 Inverse Generating function
ORM Embedding position
SRF2 = ORM + CS2
SRF1 = ORM + CS1
Special Case: Coordinate Conversion
Both SRFs use the same ORM (H not needed)

## Slide 119: Change SRF operations
Source direction vector
LTP1 rotation matrix
ORM1 Embedding direction
reference ORM Embedding position
Coordinate frame vector rotation
Target direction vector
LTP2 rotation matrix
ORM2 Embedding direction
Inverse Coordinate frame vector rotation
LTP1
LTP2
Rotation matrix
Direction Vectors

## Slide 120: Spatial operations
Validation: function for determining coordinate validity after a change SRF operation.
  valid when the coordinate falls within the valid region specification for that SRF;
  extended valid when the coordinate falls outside of the valid region specification for that SRF, but falls within the extended valid region specification for that SRF;
  defined when the coordinate falls within the domain of the CS specified for that SRF; and
  invalid when the coordinate falls outside of the CS domain of the SRF Class of that SRF Class instance.
Example UTM
  Valid region: 3 of UTM zone central meridian.
  Extended valid region: 6 of UTM zone central meridian.

## Slide 121: Abstract API

## Slide 122: SRM API
Abstract specification
  Language bindings are separate documents.
SRF objects are instances of SRFT classes.
Most operations are methods on SRF objects.
  A coordinate object only has meaning in the context of an SRF.
Hierarchical structure: Methods common to a sub-class of SRFT classes are documented in abstract base classes.

## Slide 123: SRM API object hierarchy (1 of 6)
LifeCycle Object Create
Destroy
Coordinate3D
CoordinateSurf
Coordinate2D
Direction

## Slide 124: SRM API object hierarchy (2 of 6)
LifeCycle Object Create
Destroy
BaseSRF GetCodes
GetORMCode
GetCSCode
BaseSRF2D CreateCoordinate2D
GetCoordinate2Dvalues ChangeCoordinate2DSRF EuclideanDistance
LocalSpaceRetangular2D Create
GetSRFParameters
Polar Create
GetSRFParameters
Azimuthal Create
GetSRFParameters

## Slide 125: SRM API object hierarchy (3 of 6)
LifeCycle Object Create
Destroy
BaseSRF GetCodes
GetORMCode
GetCSCode
BaseSRF3D CreateCoordinate3D
CreateDirection GetCoordinate3Dvalues GetDirectionValues ChangeCoordinate3DSRF ChangeDirectionSRF EuclideanDistance

## Slide 126: SRM API object hierarchy (4 of 6)
BaseSRF3D CreateCoordinate3D
CreateDirection GetCoordinate3Dvalues GetDirectionValues ChangeCoordinate3DSRF ChangeDirectionSRF EuclideanDistance
BaseSRFwithTangentPlaneSurface CreateCoordinateSurf
GetCoordinateSurfValues
AssociateCoordinateSurf
PromoteCoordinateSurf
EuclideanDistance
ConcreteSRF3D Create
GetSRFParameters
BaseSRFwithEllipsoidalHeight CreateCoordinateSurf
GetCoordinateSurfValues
AssociateCoordinateSurf
PromoteCoordinateSurf
CreateLocalTangentEuclideanSRF
OffsetVerticalSeparation
GeodesicDistance EuclideanDistance

## Slide 127: SRM API object hierarchy (5 of 6)
BaseMapProjectionSRF ConvergenceOfTheMeridian
PointScale
MapAzimuth
ConcreteMapProjection Create
GetSRFParameters
Celestiodetic Create
GetSRFParameters
BaseSRFwithEllipsoidalHeight CreateCoordinateSurf
GetCoordinateSurfValues
AssociateCoordinateSurf
PromoteCoordinateSurf
CreateLocalTangentPlaneSRF
OffsetVerticalSeparation
GeodesicDistance EuclideanDistance

## Slide 128: SRM API object hierarchy (6 of 6)
LocalTangentEuclidean Create
GetSRFParameters
LocalTangentAzimuthalSpherical Create
GetSRFParameters
LocalTangentCylindrical Create
GetSRFParameters
BaseSRFwithTangentPlaneSurface CreateCoordinateSurf
GetCoordinateSurfValues
AssociateCoordinateSurf
PromoteCoordinateSurf
EuclideanDistance

## Slide 129: SRM API non-object functions
CreateStandardSRF3D
Input: SRF_Code
Output: SRF3D
CreateSRFSetMember
Inputs: SRFS_Code
SRFS_Member_Code
ORM_Code
Output: SRF3D

## Slide 130: Abstract API examples
Example 1: Find the Euclidean distance between two locations.
--Note: Label in italics denotes a symbolic constant for this example --
Celestiodetic method Create ( Input: ORM_N_AM_1983_CONUS; Output: srf)
srf method CreateCoordinate3D ( Inputs -77º(/180º), +38º(/180º), 0; Output: coordinate1)
srf method CreateCoordinate3D ( Inputs +3º(/180º), +49º(/180º), 0; Output: coordinate2)
srf method EuclideanDistance ( Inputs coordinate1, coordinate2, 0; Output: distance)
-- use distance result --
coordinate1 method destroy coordinate2 method destroy srf method destroy

## Slide 131: Abstract API examples
Example 2: Change SRF representation of a location from UTM to Celestiocentric
--Note: Labels in italics denote symbolic constants for this example -- Function CreateSRFSetMember ( Input: SRFS_UNIVERSAL_TRANSVERSE_MERCATOR, ORM_N_AM_1983_CONUS, ZONE_23_NORTHERN_HEMISPHERE, Output: source_srf) Function CreateCoordinate3D ( Inputs 120, 400, 0, Output: source_coordinate) Function CreateStandardSRF ( Input: SRF_GEOCENTRIC_EARTH_1984, Output: target_srf) srf method ChangeCoordinate3DSRF ( Inputs source_srf, source_coordinate, Output: target_coordinate)
-- use target_coordinate result --
source_coordinate method destroy target_coordinate method destroy source_srf method destroy target_srf method destroy

## Slide 132: SRM API Implementation
STC Tutorial
4 - 6 PM, Tuesday, January 6
SRM for Programmers

## Slide 133: Computational considerations
Accuracy
Errors
Testing
Algorithm Design

## Slide 134: Error sources in spatial operations software
There are many possible error sources in development of software for coordinate transformations.
  Truncation errors are due to the use of a finite number of terms in an infinite series.
  Approximation error is due to approximating one function with another (simpler to compute) function.
  Iteration error is due to the use of a finite number of iterations in an iterative process.
  Formulation errors are due to the analyst developing the incorrect equations or logic – this includes improper formulations near singular points, improper treatment of signs, incorrect treatment of units and others.
  Implementation errors are due to improper coding of the correct formulation.
  Round-off errors are those caused by finite word length computers.

## Slide 135: Bounds checking
Coordinate transformations may only be valid for prescribed regions.
Both input and output should be checked for validity.
For many coordinate frameworks, the mathematical formulation may exist everywhere even though the results may be nonsensical for some regions.
Determining acceptable bounds requires an examination of distortion effects and, in some cases, computational accuracy.
This is an emerging issue for SRM standardization efforts.
The problem is multi-faceted:
  What are the acceptable bounds?
  For which applications?
  Who determines them?

## Slide 136: Distortion and computation error tradeoff
The computational complexity and efficiency of series representations depend on the number of terms used.
For map projection-based SRFs, distortion generally increases away from the origin.
Computational accuracy may be swamped by errors due to distortion.
Appropriate tradeoff of these effects are application dependent, and is central to determining validity bounds.
There is little published information to support a cogent decision on how to set the bounds.

## Slide 137: How should accuracy be specified?
Published standards for mathematical library routines set a precedent for this Issue.
  E.g., IEEE standards specify a valid operating range and accuracy for each function.
Examples of what happens when the argument is out of range:
  A negative argument for a real square root, or a zero input for a logarithm will generate error messages.
  Too large (or small) an argument may generate a warning or require special handling (overflow-underflow protection).
Computational performance (efficiency) is not specified, but is market driven.
Accuracy is specified in decimal digits (or bits of precision).
  Accuracy is specified for the worst-case application.
  Nominal applications never come close to needing full accuracy.
  No options are provided for reduced accuracy – this leads to ad hoc (non-standard) in-line replacements to reduce computation time.
Standards based implementations require bounds checking and accuracy specification.

## Slide 138: Ground rules for spatial operations algorithm development
A Spatial Operation (SO) for Earth specific applications is a
coordinate transformation, a coordinate conversion, an azimuth
determination, a distance calculation or other computations
associated with elliptical trigonometry and map projections.
GR 1: Consider the current computational environment:
- a surfeit of low cost Dynamic Random Access Memory (DRAM),
- high speed cache available,
- super scalar architectures for pipelined (parallel processing),
- very high speed processing of some standard mathematical functions,
- improved compilers consistent with pipelined processing,
- operating systems with dynamic optimization of resources,
- IEEE double precision as nominal processing mode.
GR 2: Consider the domain of application:
- develop for all regions but recognize that specific regions or
applications may require different approaches,
- do not lose sight of the fact that majority of applications are in the near Earth
region [-12, 35] kilometres (in geodetic height). This region encompasses the
lowest point of Earth bathymetry (Marianas Trench) to the limit of air breather flight.

## Slide 139: Ground rules for spatial operations algorithm development (cont’d)
GR 3: Define a meaningful error measure:
- use a Euclidean position error metric where this makes sense,
- convert angular errors to position errors,
- use a maximum position error over the entire region of interest.
- avoid the use of average absolute component errors.
GR 4: Avoid excessive accuracy:
- the SEDRIS goal is a maximum of 1mm position error over a region,
- avoid algorithms designed to yield errors like 10-08 or 10-20 if computational
resources are required to achieve such accuracies.
GR 5: Set an acceptable error goal before starting development:
- for the SEDRIS accuracy goal, 0,000 9 mm, is < 0,022 860 in, is < 1/32 in,
- note that when the maximum position error is small the component errors
are small,
- when angular errors are changed to position errors a small position
error usually implies a very small angular error.

## Slide 140: Ground rules for spatial operations algorithm development (cont’d)
GR 6: Use mathematical formulations consistent with GR1:
- use low order piecewise continuous representations when possible
(popularly called table look up). This exploits low cost DRAM,
- do not use in-line table look up for square root or transcendental
functions. It is virtually impossible to compete with built in system
functions for these,
- do use global approximations or piecewise approximation if there is
no high performance system routine. Note that, for example, sin(x) is
not sin(f(x)). Depending on f(x), sin(f(x)) may be better handled by
piecewise approximation,
- if forced to use a series, use only as many terms as required near the
expansion point and more further away from the expansion point,
- for iterative methods determine the number of iterations required
via error analysis and do not use expensive termination tests.

## Slide 141: Ground rules for spatial operations algorithm development (cont’d)
GR 7: Use good programming practices:
- modern compilers can repair bad programming practices but do
not depend on that,
- compute global constants once at start up,
- compute local constants once at the highest loop level,
- nest polynomials, etc,
- coding of the publication form of an algorithm is some times referred to
as a naïve implementation. Never code the publication form of an algorithm
without considering the computational aspects. Use trigonometric identities to
simplify, avoid power functions, logarithms, exponentials by re-formulation.
Seek competent counsel if you lack experience,
- naïve formulations and implementations are common in the literature
and even in authoritative codes. Many times the conclusions of a publication
are completely wrong due to the use of naïve implementations.

## Slide 142: Ground rules for spatial operations algorithm development (cont’d)
GR 8: Design to context:
- algorithms for computing SOs should be designed for the context in
which they are used. SO algorithms are usually not employed in isolation.
Many SO computations are followed immediately by several more to
form what is called a chain.
- all variables needed for the chain should be retained for subsequent use,
- designing for context may determine which of several procedures is
best.
Example for an ERM: Some algorithms for converting geocentric
coordinates to geodetic naturally compute the trigonometric functions of
latitude and the radius of curvature in the prime vertical to full accuracy
as part of the process. If this conversion is followed by a transformation
to a map projection these variables will be needed. A good design for the
first conversion will retain them. On the other hand some popular
algorithms for the first conversion do not naturally produce these
variables and to get them require more relatively expensive calculations.
This should influence the choice of algorithm.

## Slide 143: Ground rules for spatial operations algorithm development (cont’d)
GR 9: Software verification & computational error assessment:
- it is good practice to use authoritative data to confirm results, but do not
be overly surprised that such data bases themselves are too sparse and
are sometimes not accurate enough,
- all formulations in the SRM have closed form solutions in at least the
forward direction. These can be used to automatically generate a dense
set of test points,
- forming localized dense test sets near singular points is a good practice,
- one result of dense testing is to verify that the implementation is working
properly over its intended area of application. Formulation and coding
errors will be evident when dense test sets are used,
- converting a point, then converting that back to the original and then
repeating the process a large number of times is called circular testing.
Circular testing will most likely yield a divergent sequence of results. This
is because round-off error, truncation error and other approximation
errors are not symmetric. Circular testing is not a valid test procedure.

## Slide 144: Ground rules for spatial operations algorithm development (cont’d)
GR 10: Performance testing can be difficult :
- in the literature, operation counts and counts of square root and transcendental function
calls are often used to compare algorithms. Such a practice is generally a very poor
predictor of performance and should only be used for rough judgments,
- sometimes algorithms are tested in isolation. A loop is coded and the loop time
determined from system timing utilities. The candidate algorithm is entered into the
loop, timed for a large number of replications, the loop time removed and the average
processing time is computed. This kind of testing is called in situ testing. In situ testing
can also yield misleading results, especially for the systems as outlined in GR 1. For
the simple programs used in situ testing there is no competition for system resources
and all the power of a super-scalar architecture will be used. The performance results
may be very misleading.
- In vivo testing is performance testing in the context of a much larger application
program. In this case there will be competition for system resources and algorithm
performance may be impacted,
- while in vivo testing is always desirable it may not be possible early in a large
development program. The developer must then use the other forms of assessment
that are available while keeping in mind what might happen in the final product,
- it is always advisable to perform in vivo tests as a final confirmation of the algorithm
performance.

## Slide 145: Spatial Operations
Quality
Accuracy
Conformance Testing

## Slide 146: Quality assurance for spatial operations
Specifying the quality of spatial operations requires error determination.
The meaning of “error” depends on the context and application domain.
Potential sources of error in spatial operations include:
  formulation error, approximation error, round-off error, truncation error and other errors associated with implementing the spatial operation.
Errors of this nature should not be confused with errors arising from modeling the true shape of a celestial object (real or virtual) by an approximate shape.
In the SRM, the reference surface used to approximate the shape of a celestial object, is assumed to be exact.
  How well a reference surface approximates the shape of a celestial object is outside the scope of the SRM.

## Slide 147: The meaning of accuracy is context dependent
Accuracy Or Error In The Context Of the SRM Refers To
Computational Error And Excludes Measurement Error Effects.
In geodesy a reference set of measured points is used to develop an Earth Reference Model (ERM)--a mathematical model of the Earth.
ERMs provide a mathematical framework for spatial referencing.
The amount of position error introduced by using an imperfect reference set of measured points is a major technical issue in geodesy but is outside the scope of the SRM.
In the context of the SRM, reference models of spatial objects are taken to be exact when forming spatial reference frames.
Operations on spatial reference frames may contain inaccuracies due to:
  the use of truncated power series representations,
  round off error,
  approximations made to reduce computational complexity to speed up computations.

## Slide 148: Conformance verification for the SEDRIS implementation
A fundamental discriminator for level of conformance verification is the numerical difference between a result obtained from the mathematical specifications in the SRM and the corresponding result obtained by an implementation.
  This requires that there be a Reference Implementation.
  A data set produced by the Reference Implementation to support conformance testing is called a Reference Data Test Set.
  For this purpose, the data points obtained from the RDS are taken to be the exact or true data points.
Quantities in the Reference Data Test Set are called test points.
  Each implementation to be tested shall have provisions for recording the information needed to compare to the Reference Data Test Set to support of conformance testing
  This set of output data is called a Test Data Set.
  The difference between the data points of an Reference Data Test Set and the Test Data Set of a particular implementation is referred to as an error.

## Slide 149: Acceptance testing methodology
It is desirable to have the number of data points be relatively large and uniformly distributed over the domain of the operation being evaluated
  Else critical points, where implementation is flawed, may be missed.
  The size and spatial distribution of values in the Reference Data Test Set is important and is operation dependent.
  Once the Reference Data Test Set is specified it is relatively easy to evaluate the appropriate error metric over the whole set of values and to find the maximum error on the Reference Data Test Set.
  This maximum error is used to determine the level of compliance of a particular implementation.
Levels of acceptance
  A particular implementation should not be required to meet the standard at the highest level if this induces unnecessary complexity and cost penalties.
  In some applications, users may choose to simplify or approximate the formulations to reduce implementation and computational complexity and in particular to reduce computer processing time.
  In doing so, they are willing to accept some degradation in accuracy for a particular application domain.

## Slide 150: The Structure of SRM ISO Standard ISO/IEC 18026 (Committee Draft)

## Slide 151: Structure of the SRM ISO standard (1 of 2)
The following clauses make up this International Standard:
• Scope defines the problem area that this International Standard addresses.
• Normative references lists the standards normatively referenced in this International Standard.
• Terms, symbols and abbreviations contains the glossary of terminology not other defined in other clauses, symbology and abbreviations used in this International Standard.
Concepts contains introduction to the concepts used in this International Standard.
Coordinate systems defines a common framework for the definition of abstract coordinate systems.
Temporal coordinate systems specifies how to define coordinate systems for time.
Reference Datums, embeddings and Object Reference Models specifies ways of measurably identifying origins and other basic locations in "space" or spatial objects.
Spatial Reference Frames defines spatial coordinates systems and the Spatial Reference Frames included in this International Standard.
Vertical offset surfaces specifies surfaces which model other aspects of a spatial object such as geiods.
Notes: Introduce the EDCS Standard (an HTML document) and explain the importance and purpose of the specification clauses.
Walk through the WD5 clauses.
These 10 clauses make up the EDCS standard, plus 9 annexes --->

## Slide 152: Structure of the SRM ISO standard (2 of 2)
Operations specifies how to convert coordinates and other geometric concepts among the Spatial Reference Frames defined in this International Standard.
• Application Program Interface defines the functional interface for the operations included in this International Standard.
Registration a defined process for expanding the standardized SRM.
Conformance defines what it means for an implementation to conform to this International Standard.
And several annexes are including:
Annex: Mathematical Foundations -contains required terminology and concepts.
Annex: Implementation notes -contains some relevant computational algorithms.
Reference objects and parameters lists the parameters defining reference objects used in this International Standard including reference ellipsoids and ORMs.
Annex: Change and deprecation plan - defines a process for change and deprecation of both standardized and registered SRM concepts to ensure the long-term coherence and orderly evolution of concepts.
Annex: Conformance testing -provides guidelines for developing conformance requirements.
Bibliography lists the informative, non-standard documents referenced in this International Standard.
Terminology index index to terms defined in the body of the text.
Notes: Continue the discussion on the EDCS Standard specification document with a walk through of the EDCS standard specification annexes.
These annexes are part of the EDCS standard specification and include sections that
  Explain the relationship of the EDCS with other coding methods,
  Units of measure whose use is deprecated (not discontinued!),
  Group membership and references for definitions of EDCS Classifications, Attributes, and Attribute Enumerants, and
  Organizational Schema membership and references for definitions of EDCS Groups within the ‘General’ Organization Schema.
  A deprecation plan for the ultimate withdrawal of entries from EDCS Dictionaries.
  Abbreviations used to construct Labels.
  A bibliography that lists informative, non-standard sources referenced in the standard.

## Slide 153: SRM concept management
To support continuous evolution and growth of the SRM International Standard, a process of registration is defined, allowing for the timely addition of new concepts to the SRM.
  Registration shall not be used to modify any existing standardized or registered SRM concept.
  New SRM concepts are registered using the established procedures of the ISO International Registration Authority for Graphical Items.
  These procedures require the proposer to supply all information for a new SRM concept except for its code.
  The code shall be assigned, and the code space managed, by the ISO International Registration Authority for Graphical Items.
The following types of SRM concepts may be registered:
  CSs,
  RDs,
  RDSs,
  ORMs,
  SRF Instances, and
  SRF Sets.
Additionally, a process of deprecation will be defined for designating out-dated or inappropriate concepts from the SRM.
Notes: Explain use of existing ISO system to register EDCS codes.
We are using an established process and on-line system to register EDCS codes and thus provide a mechanism for rapid and consistent incremental growth of available EDCS dictionary entries.
We will leverage the current ISO/IEC 9973 system which is being expanded to register environmental dictionary entries in addition to its current graphical items.
We are still working out the business rules and mechanics for registering EDCS dictionary entries but we do know that we will have different labels and codes for new registered entries.

## Slide 154: Further reading
1. “Handbook for Transformation of Datums, Projections, Grids and
Common Coordinate Systems”, U.S. Army Corps of Engineers,
Topographic Engineering Center, TEC-SR-7, 1998.
2. “Department of Defense World Geodetic System 1984”, National
Imagery and Mapping Agency, Third Edition, TR8350.2, 1997.
3. “Geodesy for the Layman”, National Imagery and Mapping Agency,
on-line at http://164.214.59/geospatial/products/GandG/geolay/toc.htm.
4. Richard H. Rapp, “Geometric Geodesy Part I & II”, The Ohio State
University, Dept. of Geodetic Science & Surveying, 1993.
5. John P. Snyder, “Map Projections -- A Working Manual”, U.S.
Geological Survey Professional Paper 1395, 1987.
6. Paul D. Thomas, “Conformal Projections in Geodesy and Cartography”,
U.S. Department of Commerce, Coast and Geodetic Survey, Special
Publication 251.